## Slide 1: Stepped-Frequency Ice Radar
Don Atwood

## Slide 2: “Ice Radar” IR&D Project
Goal: Investigate the use of radar systems for identifying and characterizing the motion of ice
Use Akela stepped-frequency radar
Employ interferometric coherence to identify ice, land, and water
Use phase to determine ice velocity
Two experiments conducted:
4 April : Grand Haven Harbor Entrance
4-7 May : Keweenah Waterway, Houghton

## Slide 3: Akela RF Vector Signal Generator
Emission – Stepped Frequency Continuous Wave (SFCW)
Frequency Range – 500 MHz to 6 GHz Frequency Hopping Rate – 14 user selectable options, 20 to 90,000 per second
Power Input – 12 watts nominal
Power Output – 17 dBm nominal
Size – 4.25″ x 7.5″ x 1.5″, 1.1 lbs
Communications Interface – 10/100 Base T Ethernet
Software Interface – LabVIEW

## Slide 4: Grand Haven Experiments
Grand Haven (on shore of Lake Michigan) chosen for availability of near-shore ice
Ice present at end of channel and along-shore to south of pier
Images acquired by GoPro camera on Phantom UAV

## Slide 5: Grand Haven Experiments
Akela deployed beach side (Site #2) of jetty

## Slide 6: Grand Haven Akela Experiments
Band (GHz) | # Frequencies | Hopping Rate | Sweep PRF (Hz) | Max. Range (m) | Resolution (m) | Numscans | Label
1-6 | 4000 | 15,300 | 3.8 | 120 | 0.03 | 462 | wideband_girl
1-3 | 4000 | 15,300 | 3.8 | 300 | 0.075 | 462 | narrowband_girl
3-6 | 4000 | 15,300 | 3.8 | 200 | 0.05 | 462 | narrowband_girl2
1-2 | 4000 | 15,300 | 3.8 | 600 | 0.15 | 462 | narrowband_1_2
2-3 | 4000 | 15,300 | 3.8 | 600 | 0.15 | 462 | narrowband_2_3
3-4 | 4000 | 15,300 | 3.8 | 600 | 0.15 | 462 | narrowband_3_4
4-5 | 4000 | 15,300 | 3.8 | 600 | 0.15 | 462 | narrowband_4_5
5-6 | 4000 | 15,300 | 3.8 | 600 | 0.15 | 462 | narrowband_5_6
5-6 | 4000 | 45,000 | 11.25 | 600 | 0.15 | 1362 | narrowband_5_6_45k
2-3 | 4000 | 45,000 | 11.25 | 600 | 0.15 | 1362 | narrowband_2_2_45k

## Slide 7: Processing the Akela Radar (Part 1)
1D FFT to convert stepped frequency data into Range vs. Slow Time
Create Pulse-pair Interferogram

## Slide 8: Preliminary Akela Results
Interferometric Magnitude (left) and Phase (right) for Narrowband_1_2
Near-shore ice and “movers” seen in image
Constant phase versus slow time indicates stationary targets
But small range bins (3-15 cm) and low PRF (3.8 Hz) are ill-suited for velocity estimation.
Rapid motions are not seen in phase.

## Slide 9: Houghton Experiments
Houghton chosen for availability of moving ice and good working environment atop the Great Lakes Research Center
Akela deployed during passage of ice

## Slide 10: Houghton Experiments
Experiments coordinated with U.S.C.G. breaking ice in Keweenah Waterway
Coast Guard broke the ice and an East wind blew the ice down the waterway

## Slide 11: Houghton Akela Experiments
Band (GHz) | # Frequencies | Hopping Rate | Sweep PRF (Hz) | Max. Range (m) | Resolution (m) | Numscans | Label
1-2 | 2000 | 30,000 | 15 | 300 | 0.15 | 462 | glrc_1_2
2-3 | 2000 | 30,000 | 15 | 300 | 0.15 | 462 | glrc_2_3
3-4 | 2000 | 30,000 | 15 | 300 | 0.15 | 462 | glrc_3_4
4-5 | 2000 | 30,000 | 15 | 300 | 0.15 | 462 | glrc_4_5
5-6 | 2000 | 30,000 | 15 | 300 | 0.15 | 462 | glrc_5_6

## Slide 12: Processing of Akela (Part 2)
Alternative to more typical Pulse-Pair Interferogram
Use:
  Interferometric Coherence to distinguish between ice and water
  Interferometric Phase to monitor time-evolving velocity
Start with Range-compressed
Akela “image”

## Slide 13: Coherent Processing of Akela (Part 2)
Slow-time Axis
Step #1
Create a stack of N complex (I&Q) Akela range-compressed “images”
Each successive layer displaced one frequency sweep to the left.
Third dimension of complex array now represents N sequential time slices
Slow-time Axis
Step #2
Drilling up through each pixel, unwrap phase and perform linear regression on phase.
“Slope” is used to compute Instantaneous LOS Speed
Step #3
Use slope to remove phase gradient for each pixel.

## Slide 14: Coherent Processing of Akela (Part 2)
Slow-time Axis
Step #4
Using the Multi-temporal stack at each pixel, compute the Coherence to identify water, stationary targets and movers.
Step #5
Compute a Coherence Mask, for all coherence values less than prescribed threshold (e.g. 0.65)
Slow-time Axis
Range

## Slide 15: Akela Results
Coherence delineates between water (low coherence) and ice/land (high coherence)

## Slide 16: Akela Results
Result validation: Ice passing GLRC pier was clocked at ~4 cm/sec
Coherence mask set at = 0.65 to remove water
Use Phase slope from linear regression used to compute LOS speeds

## Slide 17: Akela Results
Coherence and Speed results for data taken at later time (with increasing ice coverage spanning the waterway)

## Slide 18: Conclusions
Akela Radar is well-suited for short-range applications (such as the Waterway), but low PRF may limit longer range applications
Any Akela application in the Arctic would require weatherization effort
Interferometry provides an alternative approach to Real-aperture Radar, providing the means to both identify non-water targets and characterize the speed of movers